260W Computer-controlled Oscillating Beam Lamp

Operation Instruction

(Please read this manual carefully before use)

Contents

Chapter 1 Safety Guidance and Technical Parameters	1

1.	Security guidance	1

2.	Technical Specifications	2

Chapter 2 Panel Operation	4

1.	An Overview	4

2.	Operation	4

1. Please use visual touch or assisted input to operate the lamp (Touch-enabled product)	4

2. Input parameters	4

3. Set the Boolean parameter	5

4. Subparameter page (parameters)	5

3.	Function operations and parameter setting	5

1.	Set the DMX address code	6

2.	Set working mode of the lamp	6

3.	Panel display settings	7

4.	Scene mode	8

5.	Set work parameters of the lamp	8

6.	Check current status of the lamp	9

Chapter 3 Description of Channels	12

1.	Channel table	12

Chapter 4 Common Failures and Matters Needing Attention	15

1.	Handling of common failures	15

2.	Matters needing attention	16

3.	Matters needing attention when RDM is used	16

4.	Installation of the lamp	17

5.	Declaration	18

# Chapter 1 Safety Guidance and Technical Parameters

## Security guidance

Warning

Please keep this manual properly for further reference. If you want to sell this product to other users, please make sure that they can get this manual as well.

Attention:

The equipment has been well packaged before it is delivered out of the factory. Please be sure to operate the equipment according to the user's manual. We will not be responsible for machine failure caused by man-made reasons.

- This lamp can only be used in dry indoor areas.

- The lamp shall be installed and operated by professionals.

- Don't allow children to operate the machine.

- Use safety ropes to fix the equipment and lift its bottom when you move the lamps.

- The lamp must be installed in well ventilated places at least 50 cm from the adjacent plane.

- Ensure that the ventilation holes are smooth so that the lamp will not be too hot during its operation.

- Ensure that the power supply voltage is consistent with the required power supply voltage of the equipment before your operation.

- Please connect the electric conductor with the ground to prevent electric shock.

- Please do not operate the lamp in environments above 40℃ or below 0℃.

- Do not connect the lamp directly to the dimming device.

- Small amount of smoke or odor may appear when the new lamp is used. The smoke or odor will disappear after 15 minutes.

- Please do not place flammable objects next to the lamp when it is used so as to prevent fire disaster.

- Please check carefully whether the power cord is damaged before you start the lamp; be sure to change it if there is any damage.

- Surface temperature of the lamp during its operation may reach 90℃. please do not touch it with your bare hands.

- Do not allow conductive bodies such as flammable liquid, water or metal to enter the interior of the lamp so to avoid electric shock or fire. If foreign bodies enter the lamp, please cut off the power immediately.

- Do not operate the lamp in dirty and dusty environments; clean and maintain the lamp regularly.

- Do not touch the electric wire when the lamp is used so as to prevent electric shock. 

- Do not wind the power cord with other wires.

- The distance between the lamp and irradiation surface should be larger than 12M.

- Turn off the power before you replace the fuses or lamp bulbs.

- Please use the same model number when you replace the fuse or lamp bulb.

- If there is a serious failure, please stop using the lamp immediately.

- Please do not start the lamp repeatedly.

- Please change shells, lens or ultraviolet filters of the lamps in time if they are obviously damaged.

- There is no available parts in the lamp, so please do not open the shell of the lamp without permission.

- Do not operate the machine by yourself. Operations of non-professionals may damage the lamp of lead to its failure to working. If you need to repair the machine, please contact the nearest authorized service center.

- Please turn off the power supply when the lamp is not used for a long time or when you repair the machine.

- In order to avoid fire or electric shock, please do not expose the lamp to rain or damp areas.

- The lamp bulb may explode under high temperature; please do not turn on the lamp within 15 minutes after power failure.  

- Please replace lamp bulbs in time if they are damaged, deformed by heat or exceed their service life.

- Do not look directly at the lamp while it is operated.

- The lamp bulb will be hot when it is used, so do not touch it with your bare hands.

- Do not operate the machine when the lamp bulbs are not equipped with a protective cover or when its shell is damaged.

## Technical Specifications

- Light source: 260W

- Expected life of lamp bulbs: 2000 hours

- Color temperature: 7800K

- Voltage: AC100-240V,50/60HZ

- Total power: 400W

- Power port: Input/output port of Power Connector

- Signal interface: Three-core DMX/RDM signal input/output

- Advanced optical systems ensure clear image quality.

- Beam angel: 0-2°

- Control panel: LCD color panel +5 buttons; Chinese and English display interface;

- Control mode: DMX512, RDM, self-propelled, master-slave, voice control functions

- Control channel: 16CH

- X-axis/Y-axis: 16-bit precision scanning; photoelectric reset system is used for horizontal and vertical direction of X-axis 540° and Y-axis 270°. Accidental collision error can be automatically retrieved and reset.

- Color disc: One fixed color disc; a total of 13 kinds of colors (including white); the two-way rainbow effect can achieve half-color, panchromatic, single and double color gradient and slow motions in positive and negative directions. It also has Hall, magnet positioning and automatic error correction function in any angle.

- Fixed pattern plate: One fixed pattern plate, 10 kinds of metal patterns +3 kinds of glass patterns. It also has Hall, magnet positioning and automatic error correction function in any angle.

- Dual Prism: It is equipped with a bi-directionally rotated and stacked 8 prism and a 16+8 Prism.

- Stroboscopic: Mechanical stroboscopic design is used; the stroboscopic frequency is as high as 1 ~ 14 times/second; the stroboscopic frequency speed can be adjusted arbitrarily and the smooth dimming is between 0% and 100%.

- Independent atomizing effect

- Independent seven-color sheets

- Dust-proof and oil-proof design

- Electronic ballast

- Bubble point system: The long-distance lamp bulb control system is designed to intelligently control the openness and closure of lamp bulbs control system in distance and effectively extend the service life of the lamp bulb.

- Speed regulation through intelligent fan: Intelligent fan speed control: The fan will automatically reduce its speed and reduce the noise of the fan when there is no point bubble or the lamp is under the strobos-closed light state so as to create good performance environments.

- Use DMX to connect and update the software.

- Work environment

Maximum tolerable ambient temperature: 45°C

Maximum tolerable surface temperature: 65°C

The lowest acceptable operating temperature: -5°C

# Chapter 2 Panel Operation

## An Overview

The schematic diagram of lamp panel is shown in Figure 1. The upper title shows names of the lamps and the lower part in the status bar, which shows signals of the current lamps and states and faults of the lamp bulb (“ERR” will be displayed when there is no fault information; otherwise, “NOR” will be displayed) and so on.

This lamp supports DMX/RDM protocol. When the lamp is searched by the RDM console, the three letters "RDM" will appear on the panel to indicate that the lamp is enumerated normally.

In order to display and operate similar “Android operating system”, you can use your fingertip or blunt object to click corresponding items.

Note: Do not use sharp objects to click the display so as not to damage it.

Figure 1 Schematic diagram of the display panel

## Operation

### 1. Please use visual touch or assisted input to operate the lamp (Touch-enabled product)

- The left zone is TFT display area and the touch area. Click the panel with your finger or hard objects with dull surface and you can set parameters or view the status and do other operations.

- The right area is used for auxiliary input. If you do not use the touch function of TFT, you can use the auxiliary input to select the items you want to set or view and complete the operation.

### 2. Input parameters

If values need to be input into the selected parameter items, the window as shown in Figure 2 will appear:

Fig 2. Number setting interface

- Set the value: You can directly pull the slider to quickly set the required value or click the "up" or "down" button on the right to set the required value accurately or use the auxiliary input to set related values.

- Apply the value: After data are well set by the "up" or "down" button, if you press the "Apply" button in the lower left corner, the value will be sent to the lamp button immediately, but it is not saved at that time.

- Save the value: Click the "OK" button in the lower right corner to save the current value to the internal memory. The saved values will be applied to the lamp next time you turn the lamp on.

### 3. Set the Boolean parameter

- When the parameter is set to a Boolean value (such as ON or OFF), you only need to click corresponding items directly to switch the parameters. The modified parameters will be saved to the internal memory. Press the parameter option on the right and the corresponding options will become gray. After you release your hand, corresponding parameters will be changed and saved. If the parameter option is not the parameter you want to change, you can move your finger to another part of the screen and corresponding parameters will not change.

- Important Boolean parameters can be set through the window, as shown in Figure 3 below:

Figure 3 Confirm the input window

### 4. Sub-parameter page (parameters)

## Function operations and parameter setting

Enter the setting interface as shown in Figure 6-1:

- In the main interface, you can enter corresponding parameter setting interfaces by selecting the six buttons.

- In the parameter setting interface, you can press the blue option on the left to quickly switch to other setting interfaces.

### Set the DMX address code

DMX address and channel mode can be set through the page shown in Figure 6-1.

The menu settings of lamps optimize the address setting. Operations for several kinds of address setting are shown as follows:

- Select “Previous” or “Next”, the address code of the precious one or the next one will be automatically calculated according to the current address code and channel data. They can be set quickly;

- Click the address code value and you can enter the numeric editing window where you can set any valid address codes. The lamp will automatically obtain current channel numbers of the lamp and automatically filter unusable address codes (512- current channel number).

- The lamp supports RDM protocol. You can set the address code of the lamp through RDM remotely.

Two buttons are provided:

- Channel mode: Different channel modes can be selected circularly;

- Lamp reset: Reset all motors.

### Set working mode of the lamp

Operations modes of the lamp can be set to control the lamp bulb according to the page shown in Figure 6-2. The lamp supports four operation modes (DMX mode, self-propelled mode, voice-activated mode and scene mode). Please refer to the previous section for parameter value setting. Detailed parameters are described as follows:

Operation mode

| DMX mode | Under the console mode, it can receive DMX signal and RDM signal. Under the console mode, it can receive DMX signal and RDM signal. |
| --- | --- |
| Self-propelled mode | The lamp will be operated automatically according to the built-in program. |
| Voice-activated mode | When the lamp detects strong sounds, the lamp will automatically run a scene according to the built-in program, otherwise, the last scene will continue. |
| Scene mode 01 | The lamp operates according to the scenes set; it supports the customized editing of up to 10 scenes at most. |
|  | 1~10 | Output specified scenarios |
|  | Automatic operation | Automatically output scenes in the sequence of setting scene time (not 0). Scenes with time of 0 will be automatically ignored. |
| Master-slave choice | It will become effective when it is not under DMX mode; please select data output mode and the lamp will automatically detect DMX status and automatically switch output to prevent data conflicts. |
|  | Console | The lamp will be operated according to the built-in program; if DMX has no signal, data will be output (synchronization); otherwise, no data will be output. |
|  | Slave | The lamp will be operated according to the built-in program and will not output data (it will not be synchronized with other lamps). |
|  | Automatic operation | If DMX has no signal, lamp will be operated according to the built-in program; otherwise, the lamp will be operated according to the DMX signal. |
| On-off operation of the lamp bulb | (Light sources of lamp bulbs) A confirmation dialog box will pop up; select "sure" to confirm the current operation. Then, switch on or off the lamp bulb and the time interval shall be set to be 30 seconds. |
|  | Close | Output of the current lamp bulb is turned off. |
|  | Open | The current light output is turned on. |

Scene mode is suitable for single lamp or small numbers of scenes. You only need to output fixed scenes or operate a simple program. The console may not be connected; you only need to edit it on the scene page.

If the light source of the lamp is the lamp bulb, you need to wait for 10 minutes after you turn off the lamp bulb. You can turn on the lamp bulb then.

### Panel display settings

The lamp supports Chinese-English settings and upside-down display. You can set corresponding parameter according to operations shown in Figure 6-3. Specific menu contents are shown in the table below:

Display settings

| Language | Set languages displayed |
| --- | --- |
|  | English | English display |
|  | Chinese | Chinese display |
| Screen protection | Set screen display content or mode if there is no operation on the screen within 30 seconds. |
|  | Close | Keep the last operation page; the screen is on. |
|  | Mode 1 | The screen is off |
|  | Mode 2 | Black screen; address code of current lamp will be displayed on the bottom left corner. |
|  | Mode 3 | Display the trademark information, address code and operation mode. |
| Screen rotation | Set the display direction of the screen |
|  | Close | Non-reverse display |
|  | Open | Reverse display |
|  | Automatic | Automatically detect lamp direction and switch the display direction. |
| DMX indication | Set the indication mode of DMX signal indicator lamp |
|  | Mode 1 | It lights up when there is a signal and goes off when there is no signal. |
|  | Mode 2 | It goes off when there is a signal and lights up when there is no signal. |
|  | Mode 3 | If flashes when there is a signal and goes off when there is no signal. |
| Signal indication brightness | Set the brightness of the signal indicator |
|  | 1~10 | 10 grades |
| Screen backlight | Set the brightness of the screen backlight after there is no operation for 10 seconds. All lights will be on during operation. |
|  | 1~10 | 10 grades |
| Touch switch | Select whether to disable the touch screen; when the screen touch is accidentally damaged, you may disable the touch function and use the auxiliary input to set the lamp. |
| Touch-screen calibration | When the screen touch is not accurate, you can enter the correction page to correct the screen. |

The lamp supports touch operation. If the touch screen does not work, you can enter the calibration page to rectify the touch precision of the touch screen again. Under normal situations, you should not enter this page. If the touch screen is damaged, please select “Disable Touch Switch”.

### Scene mode

Enter the page displayed on Figure 6-4 and the lamp will enter the scene editing mode. On this page, the lamp will not receive DMX console data. The edited data will be reflected to the lamp instantly.

Contents of the page are based on the currently selected channel and the channel contents and orders displayed are the same as those of the lamp channel table. 10 scenes can be edited on this page and they are shown in the table below:

Scene mode

| Scene selection | Select the scene to operate on at present |
| --- | --- |
|  | 1~10 | Setup formats for 10 scenes |
| Scene time | Set the retention time of the current scene on automatic mode; unit: 0.1 second |
|  | 0 | The current scene does not participate in the automatic scene output |
|  | 1-255 | From 0.. 1 to 25.5 seconds |
| 1. X-axis | 0-255 | Set data for each channel so that the display contents and orders can match the channel table for the lamp |
| …… | 0-255 |  |
| …… | 0-255 |  |
| N. function | 0-255 |  |

If effective reset data are edited by the reset channel in the scene, the lamps will be reset. However, after that, values of corresponding reset channels will be automatically reset to zero so as to prevent multiple consecutive resets.

Check this page to obtain the current channel table order of the lamp. Refer to the detailed channel description for channel data.

### Set work parameters of the lamp

Enter the page shown in Figure 6-5 to adjust on-field parameters of the lamp and to facilitate field installation of the lamp:

Advanced settings

| X-axis reverse | Set the X-axis rotation direction |
| --- | --- |
|  | Close | Not reversed |
|  | Open | Reverse |
| Y-axis reverse | Set the Y-axis rotation direction |
|  | Close | Not reversed |
|  | Open | Reverse |
| Optocoupler calibration | Set whether the lamp can detect lost synchronization of X-axis and Y-axis and correct them. |
|  | Close | No position correction after lost synchronization |
|  | Open | Automatically correct the position after lost synchronization and record failures for lost synchronization |
| X-axis offset | Set the position of the null point at X-axis of the lamp |
|  | 4-150 |  |
| Y-axis offset | Set the position of the null point at Y-axis of the lamp |
|  | 4-48 |  |
| Data Retention | Set the output state of the lamp when the lamp has no DMX signal. |
|  | Close | No signal; the motor and light source return to the position and state when it is well reset. |
|  | Open | No signal; keep the last DMX data output |
| Light-up pattern | Set the way that the lamp bulb is started after it is powered on |
|  | Power-on bubble | Start the lamp bulb first after it is powered on and then reset the lamp 30seconds later. |
|  | Reset completion bubble opened | Reset the lamp after it is powered on for three seconds; open the lamp bulb after it is well reset. |
|  | Start bubble manually | After it is well reset, manually turn on the lamp bulb bulbs through the menu or the console. |
| Factory settings | After the confirmation box pops out, you should select “SURE” and lamp parameters will return to the factory settings. |

When the power-on bubble mode is used, the lamp will wait for the lamp bulb for 30 seconds to fully start the lamp bulb. As long as the internal voltage is stable enough, the reset program shall be started again. If the site has stable electricity capacity, the power-on lamp bulb mode is recommended.

If the lamp fails to correct the position, please check whether the “Optocoupler calibration” is turned off.

After the signal is removed, if the position of the lamp is not output according to the set value, please check “Data Hold” setting first.

After the offset values of XY axes are set, please control XY with the maximum stroke and then check whether X and Y will not hit the positioning rod or shell after it is well set.

### Check current status of the lamp

You can check the information and real-time status of the lamp in the page shown in Figure 6-6 and to obtain the usage status of the lamp. If you need after-sales service, please provide the status information displayed on this page for judgment. The information is shown in the table below:

Status information

| Motor information | Display the information status of all motors and signals of the lamp |
| --- | --- |
|  | Hall | If it is not displayed, it means that the motor is not corrected through Hall correction. 0 means that the motor has been away from the correction position point while 1 means that the motor is at the correction position point. |
|  | Status | Display reset completion state of the motor |
|  | X-axis | Display the real-time position fed back by the X-Axis Optocoupler |
|  | Y-axis | Display the real-time position fed back by the Y-Axis Optocoupler |
|  | Optocoupler | Display the electrical level state of optocoupler on X-Axis and Y-Axis. The binary system is used. |
| Failure/status record | Display recent 8 fault records when the lamp is reset and operated; fault records will not be saved after power is off. It is valid in the current electric cycle. |
|  | Failure data | Total number of faults detected after power is on |
|  | 12: :03 | Power-on time when the fault appear; unit: minute. |
|  | Hall failure | No effective Hall signal is detected by the motor when corresponding motor is reset |
|  | Hall short circuit | The Hall signal of the motor is always valid when corresponding motor is reset. |
|  | Optocouple failure | No effective Optocoupler signal is detected when the corresponding motor is reset. |
|  | Step failing out | The corresponding motor steps out during operations of the corresponding motor. |
|  | Hit the rod | Hit the positioning rod when corresponding motor is reset. |
|  | Failure of the lamp bulb | The lamp bulb accidentally goes off. |
|  | Sensor fault | Temperature sensor has abnormal signals. |
|  | Fan fault | The main fan does not work normally. |
| Lamp status | Display key status data for the current lamp for reference |
|  | Communication | 0~100%; Communication quality of internal data links of the lamps |
|  | Error count | The total number of error frames detected after power is on. |
|  | Light source temperature | Display the temperature of the current light source. "--" means no detection. |
|  | Display panel temperature | Display the temperature of the current display board or temperature of nearby places |
|  | Sensor 1 temperature | Display the current motherboard temperature or the ambient temperature at the location where the main board is installed |
| Version information | Display the information and version of the current lamp; serve as an important reference for after-sales maintenance |
|  | Equipment | Name of the lamp; it is the same as the RDM device information |
|  | Model number | The model number of lamp; it is same as the model number information of RDM |
|  | Display board | The firmware version and serial number of the display board |
|  | Main board 1 | The firmware version and serial number of the motherboard 1 |
| Light source time | Record the total cumulative time of lamp sources turned on; the unit is minute. It can be manually cleared by users and used as a reference time for regular maintenance of light sources. |
| Lamp time | Record total lamp opening time. Unit: minute. It can not be cleared. |

# Chapter 3 Description of Channels

## Channel table

The lamp has 16 channel modes.

Orders of channels can be checked in the scene mode. The channel mode can be set in the "Address Settings" page and detailed data are shown in the following table:

Channel table

| Channel | Name | Value | Description |
| --- | --- | --- | --- |
| CH1 | X-axis | 0-255 | 0-540° |
| CH2 | Y-axis | 0-255 | 0-270° |
| CH3 | X-axis fine tuning | 0-255 |  |
| CH4 | Y-axis fine tuning | 0-255 |  |
| CH5 | XY speed | 0-255 | From fast to slow |
| CH6 | Pulverization | 0-127 | No |
|  |  | 128-255 | Insert the atomization |
| CH7 | Strobing | 0-3 | Close the light |
|  |  | 4-103 | Pulse strobe from slow to fast |
|  |  | 104-107 | Open the light |
|  |  | 108-207 | Gradual strobing from slow to fast |
|  |  | 208-212 | Open the light |
|  |  | 213-251 | Random strobing from slow to fast |
|  |  | 252-255 | Open the light |
| CH8 | Dimming | 0-255 | 0-100% Dimming |
| CH9 | Color |  |  |
|  |  | 0-9 | White light |
|  |  | 10-14 | White light + Color 1 |
|  |  | 15-19 | Color 1 |
|  |  | 20-24 | Color 1 + Color 2 |
|  |  | 25-29 | Color 2 |
|  |  | 30-34 | Color 2 + Color 3 |
|  |  | 35-39 | Color 3 |
|  |  | 40-44 | Color 3 + Color 4 |
|  |  | 45-49 | Color 4 |
|  |  | 50-54 | Color 4 + Color 5 |
|  |  | 55-59 | Color 5 |
|  |  | 60-64 | Color 5 + Color 6 |
|  |  | 65-69 | Color 6 |
|  |  | 70-74 | Color 6 + Color 7 |
|  |  | 75-79 | Color 7 |
|  |  | 80-84 | Color 7 + Color 8 |
|  |  | 85-89 | Color 8 |
|  |  | 90-94 | Color 8 + Color 9 |
|  |  | 95-99 | Color 9 |
|  |  | 100-104 | Color 9 + Color 10 |
|  |  | 105-109 | Color 10 |
|  |  | 110-114 | Color 10 + Color 11 |
|  |  | 115-119 | Color 11 |
|  |  | 120-124 | Color 11 + Color 12 |
|  |  | 125-129 | Color 12 |
|  |  | 130-134 | Color 12 + Color 13 |
|  |  | 135-139 | Color 13 |
|  |  | 145-149 | Color 13 +white light |
|  |  | 150-203 | Forward flow from fast to slow |
|  |  | 204-255 | Reverse flow from slow to fast |
| CH10 | Pattern | 0-4 | White light |
|  |  | 5-9 | Pattern 1 |
|  |  | 10-14 | Pattern 2 |
|  |  | 15-19 | Pattern 3 |
|  |  | 20-24 | Pattern 4 |
|  |  | 25-29 | Pattern 5 |
|  |  | 30-34 | Pattern 6 |
|  |  | 35-39 | Pattern 7 |
|  |  | 40-44 | Pattern 8 |
|  |  | 45-49 | Pattern 9 |
|  |  | 50-54 | Pattern 10 |
|  |  | 55-59 | Pattern 11 |
|  |  | 60-64 | Pattern 12 |
|  |  | 65-69 | Pattern 13 |
|  |  | 70-125 | Forward flow from fast to slow |
|  |  | 126-130 | Stop |
|  |  | 131-190 | Reverse flow from slow to fast |
|  |  | 191-195 | Pattern 1 shakes |
|  |  | 196-200 | Pattern 2 shakes |
|  |  | 201-205 | Pattern 3 shakes |
|  |  | 206-210 | Pattern 4 shakes |
|  |  | 211-215 | Pattern 5 shakes |
|  |  | 216-220 | Pattern 6 shakes |
|  |  | 221-225 | Pattern 7 shakes |
|  |  | 226-230 | Pattern 8 shakes |
|  |  | 231-235 | Pattern 9 shakes |
|  |  | 236-240 | Pattern 10 shakes |
|  |  | 241-245 | Pattern 11 shakes |
|  |  | 246-250 | Pattern 12 shakes |
|  |  | 251-255 | Pattern 13 shakes |
| CH11 | Prism | 0-63 | Remove the prism |
|  |  | 64-127 | Insert prism 1 |
|  |  | 128-191 | Insert prism 2 |
|  |  | 192-255 | Insert Prism 1 and Prism 2 |
| CH12 | Autorotation of prism 1 | 0-64 | 0-400° |
|  |  | 65-127 | Forward flow from fast to slow |
|  |  | 128-191 | Stop |
|  |  | 192-255 | Reverse flow from slow to fast |
| CH13 | Autorotation of prism 2 | 0-64 | 0-400 degrees |
|  |  | 65-127 | Forward flow from fast to slow |
|  |  | 128-191 | Stop |
|  |  | 192-255 | Reverse flow from slow to fast |
| CH14 | Focusing | 0-255 | From far to near |
| CH15 | Seven colors | 0-127 | No |
|  |  | 128-255 | Insert seven colors |
| CH16 | Reset/lamp bulb | 100-105 | Turn off the lamp bulb after more than three seconds. |
|  |  | 200-205 | Turn on the lamp bulb after more than three seconds. |
|  |  | 210-215 | Reset the XY after more than three seconds. |
|  |  | 220-235 | Reset effects after more than three seconds |
|  |  | 240-255 | Reset effects after more than three seconds |

# Chapter 4 Common Failures and Matters Needing Attention

## Handling of common failures

The lamp contains the microcomputer circuit boards, high voltage power supply and other professional parts. In order to ensure your safety and the service life of the product, non-professionals should not dismount lamps and related accessories.

#### The lamp bulb is off (except LED light source)

Possible reasons: Lamp bulb is not completely cooled or the lamp bulb reaches its service life. Please handle them as follows:

- The lamp bulb is not fully cooled down because of abnormal operation. The lamp shall be cooled down for more than 10 minutes so that its inside parts can be operated normally. Then, start the power supply again.

- Check whether the lamp bulb has reached its service life and replace the new lamp bulb in time.

- Check whether the lamp bulb and lines of the lighting apparatus suffers from electric leakage, falling or poor contact;

- Change new lamp lighter.

#### The light beam is dim

Possible reasons: The lamp bulb has been used for a long time or the light path is not clean. Please handle them by using the following methods:

- Check whether the lamp bulb has reached their service life. Please change new lamp bulb.

- Check whether optical parts or the lamp bulbs are clean and whether there is dust accumulated on the lamb bulb and optical devices. Clean and maintain the lamb bulbs and other parts regularly.

#### Blurry pattern projection

- Check whether the electronic focusing channel value is appropriate for the current projection distance.

#### The lamp works intermittently

Possible reasons: Internal circuits are under the protection state. Please handle this matter according to the following methods:

- Check whether the fan is running properly or has been dirty, which can lead to higher internal temperature;

- Check whether the internal temperature control switch is in a closed state;

- Check whether the lamp bulb has reached service life and replace it with a new lamp bulb.

#### The lamp is not controlled by the console after it is reset normally.

Possible reasons: The signal lines have faults or parameters of the lamp are not set normally. Please handle this matter according to the following methods:

- Check the starting address code and the connection situation of DMX signal line (whether the signal line cable is in good condition and the connection ports have been loosed or not).

- Install a signal amplifier and a 120-ohm terminal resistor;

#### The lamp can not be started

Possible reasons: Possible reasons: Poor line contact. Please handle this matter according to the following methods:

- Check whether the fuse wire on the power input socket has been fused. If so, please replace the fuse wire in time;

- Vibration of the lamp in long distance transportation leads to bad contact;

- Check the input power supply, computer board and other plug-in devices.

## Matters needing attention

- Check whether the power supply at local areas can meet rated voltage requirements and whether the leakage protector and over-current protector can meet the load requirements;

- Do not use the power cord whose insulation layer has been damaged. Do not lap the power cord on other wires.

- Lamp refrigerates through strong wind, which may lead to the accumulation of dust. Therefore, the lamp, especially its heat vent, shall be cleaned every month, otherwise, the it will be blocked by dust accumulation, which may lead to poor heat dissipation and abnormal situation of the lamp.

- When the lamp is installed, the fixing screws must be tightened and safety cable must be equipped. They shall be checked regularly.

- When the lamp is installed and positioned, the site on the surface of the lamp shall be 10 meters away from any inflammable explosive material, be 2.5 meters away from the light objects. Please do not install the lamp directly on surfaces of inflammable materials.

- The continuous working time of the lamp should not exceed 10 hours and the interval between consecutive starting time should not be less than 10 minutes, otherwise, lamp bulbs may not be normally triggered because of overheating protection;

- The closing time of the on-off valve should not exceed 5 minutes. If the light needs to be turned off for a long time, the light gun shall be turned off by the console (the light gun control channel).

- In order to ensure that many lamps can better comply with scene effects, the lamps should not be kept in the present uncompleted scene before it starts the next scene. This state should be less than three minutes and you should ensure that more than one lamps can be operated synchronously;

- When the lamps are used, if some lamps become abnormal, you should stop using them immediately so as to prevent the occurrence of other failures.

## Matters needing attention when RDM is used

RDM is an extended version of DMX512-A protocol a Remote Device Management protocol. Traditional DMX512 protocol communication is a one-way communication. This protocol is based on RS-485 bus, a time-sharing multi-point, half-duplex protocol which only allows one port to output to the console at a time. Therefore, you should pay attention to the following matters when you use RDM:

- Use a console or host device that supports RDM protocol console;

- Bi-directional amplifier shall be used because traditional unidirectional amplifiers are not suitable for RDM protocol, which requires feedback data. Unidirectional amplifier will block the returned data and lead to the failure in searching for the lamp.

- All lamps must be set to DMX mode and there shall only be one host on one signal line;

- A 120ohm impedance matching resistor must be inserted between terminal 2 and terminal 3 of the terminal plug. When there are long signal lines, the reduction of signal reflection will make differential signals more stable, which is beneficial to improving the communication quality.

- In the case where lamps can be controlled by DMX but can not be searched by RDM, you should check the signal amplifier first. Then, you need to check whether either signal line 2 or signal line 3 is not well contacted.

## Installation of the lamp

Use RS-485 cable conforming to specifications (shielding function, 120ohm characteristic impedance, 22-24 AWG, low capacitance) shall be used. Do not use microphone cables or cables with different specified characteristics. Terminals must be connected through a 3-pin or 5-pin XLR male/female connector. (Minimum 1/4 W).

Important hint: The wires should not contact each other or be connected with metal enclosures

Fig. 4 Schematic diagram for DMX signal line connection

The lamps can be placed horizontally, hung diagonally and hung upside down. Be sure to install them correctly when they are hung diagonally and upside down.

As what is shown in Figure 5, before you position the lamps, you should confirm that the installation site is stable. If the lamps are hung reversedly, you must ensure that the lamps should not fall down from the support frame. Therefore, you need to pass a safety rope through the support frame and the handle of the lamp so as to ensure the safety and prevent the lamps from falling down or sliding.

When the lamps are installed and debugged, no pedestrian is allowed to pass underneath. You should check the safety ropes regularly to see whether they are worn and whether the hook screws    are loose.

Our company will not take any responsibility for consequences caused by falling lamps which are not stably installed.

Fig. 5 Schematic diagram for the lamp hung upside down

## Declaration

This product has intact performance and complete packaging when it is delivered out of the factory. All users should strictly follow warnings and operating instructions stated above. Any damage caused by our using this product improperly will not be guaranteed by our company. The dealer will not be responsible for any malfunction or problem caused by operations done not according to the operation manual.

This manual is subject to technical changes without prior notice.