Laser Show System

User Guide

（Please read this product manual carefully before using）

Product models, specifications and technical parameters are subject to change without notice

WARNING

Thank you for purchasing this product. For better using it in a correct way, please read this user manual carefully, in case of any unsafe for human being or cause any damage for lighting fixture.

Please check product carefully when receiving it, and check if there’s any problem caused during transportation.

You should find inside the laser carton the following items:

- Laser

- Power Cable

- User Manual

CAUTION

The manufacturer will not accept liability for any resulting damages caused by the non-observance of this manual or any unauthorized modification to the equipment.

- Make sure that the best temperature range is: 20~35°C.

- Never use laser direct to people, especially for eyes in case of any harm.

- Make sure that the available voltage is between AC220V~240V, and make sure the ground cable is always reliable.

- Please don’t turn on or off frequently, in case of reducing the normal lifespan of laser.

- As per solid state laser diode features, better avoid laser working for long time. After using 3 hours, please turn off the light for 15-min break, and re-start after cooling off completely.

- Don’t touch the laser diode mirror, in case affecting the lighting effect.

- Don’t disassemble lighting fixture, if there’s any problem, please ask a qualified engineer inspect the equipment before operation again.

（Before using，please read the user manual carefully.）

Dear user：

This is product integrates many advanced technologies like optics, electronics, digital graphic processing, especially designed for dancing halls and DISCO. According to music rhythms, built-in beam program can be activated; if using smoke, light curtain wall and time tunnel can be formed to create a colorful and fantastic laser world.

NOTICE

1. The best temperature range of using laser：20～35℃。

2. Do not reflect to the eye directly in case of hurting.

3. Do not use the laser over AC220V～240V and please make sure reliable grounding.

4. Do not turn on and turn off frequently; this will affect the laser’s normal life.

5. Based on the working character of solid state laser, please try not to work for a long time. If the laser works continuously for three hours, please turn off the laser 15 minutes. After the laser is cold, start to turn on again.

6. Do not use hands to touch the lens in case it will affect the effects.

- If there appears breakdown, please ask experts to repair; do not   remove the laser yourself.

- Attention：Destroy the laser or tear up the warranty label artificially, it’s all beyond warranty scope. Please read the warranty rules.

1. Operating Instructions

| DIPSWITCH CHART | FUNCTION |
| --- | --- |
| #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | #10 |  |
| X | X | X | X | X | X | X | X | X | x | SOUND ACTIVE |  |
| 1 | X | X | X | X | X | X | X | x | x | AUTO MODE |  |
| 1 | 1 | x | x | x | x | x | x | x | x | Animatiom |  |

Sound control 			    Auto working

Animation                  DMX512  address=001

Binary value

DMX512  address=8+32+128=168

DMX512  address=4+128=132

Form I The international standard DMX 512 Signal suitable for laser with 12 channels. The detailed control function is shown below:

| Channel | Function | Value | Description |
| --- | --- | --- | --- |
| CH1 | Laser control mode | 0-49 | Close laser |
|  |  | 50~99 | Sound activation group ,3-10 invalid |
|  |  | 100~149 | automobile group,3-10 invalid |
|  |  | 150~199 | Animation group,3-10 invalid |
|  |  | 200-255 | DMX 512 control |
| CH2 | Switch color | 0~4 | closed down |
|  |  | 5-255 | Switch color |
| CH3 | Switch patterns | 0~255 | 128Pattern(0~255) |
| CH4 | Moving pattern | 0~255 | Vertical move |
| CH5 | Moving pattern | 0~255 | Horizontal mov |
| CH6 | Horizontal move | 0~255 | Vertical move |
| CH7 | Vertical move | 0~255 | Horizontal move |
| CH8 | Pattern rotate | 0~127 | Manual control counter-clockwise rotation |
|  |  | 127-189 | Auto counter-clockwise rotation |
|  |  | 190-255 | Auto clockwise rotation |
| CH9 | Stretch | 0~4 | None |
|  |  | 5-85 | Small to big |
|  |  | 86-170 | Big to small |
|  |  | 170-255 | Random |
| CH10 | Zoom | 0-255 | Small to big |
| CH11 | Gradually draw | (0~255)/21 | gradual change |
| CH12 | flicker effect | (0~255) | Fast to slow |

Form                     DMX Address form